# Introduction
The purpose of this design document is to outline the different features of the multi-tool. The document will outline the system architecture and the different technologies that will be utilised, provide diagrams to illustrate the flow of the different interconnected systems and provide illustrations of the various screens that the system will have.
# System Architecture
## Hardware Architecture

### Raspberry Pi Zero 2 W
The Raspberry Pi Zero 2 W is a micro-computer. The board hosts a quad-core 64 bit ARM central processing unit (CPU) and 512mb of random access memory (RAM). It has built in Wi-Fi and Bluetooth 4.2 which makes it ideal for this project. The board has a 40 pin general-purpose input/output (GPIO) header allowing for inter-connectivity between the different modules in the project. There are also 3 ports on the board, one for HDMI and the other 2 for micro-USB.
### Waveshare PN532 NFC HAT
The Waveshare PN532 is a Raspberry Pi HAT designed to allow development boards to utilise Near Field Communications (NFC) and Radio Frequency Identification (RFID) technologies. The HAT has a 40 pin GPIO header and supports various NFC and RFID cards such as MIFARE and NTAG2.
### Anavi Infrared pHAT
The Anavi Infrared pHAT allows the Raspberry Pi to utilise infrared technologies though the use of its transmitters a receiver. This board has a 40 pin GPIO header and also contains sensor modules for temperature, humidity, barometric pressure and light.
### Waveshare 3.5" IPS Touch Screen
This touch-screen IPS display from Waveshare will be used to show the system menu to the pen-tester. The screen uses a 26 pin header, as opposed to the 40 pin headers that some of the other modules use.
### Battery (?)
## Software Architecture
*Insert Software Architecture here!*
### MiniPy

# References