# Introduction
The purpose of this design document is to outline the different features of the multi-tool. The document will outline the system architecture and the different technologies that will be utilised, provide diagrams to illustrate the flow of the different interconnected systems and provide illustrations of the various screens that the system will have.
# System Architecture
## Hardware Technology Stack

### Waveshare 3.5" IPS Touch Screen
This touch-screen IPS display from Waveshare will be used to show the system menu to the pen-tester. The screen uses a 26 pin header, as opposed to the 40 pin headers that some of the other modules use.
### Raspberry Pi Zero 2 W
The Raspberry Pi Zero 2 W is a micro-computer. The board hosts a quad-core 64 bit ARM central processing unit (CPU) and 512mb of random access memory (RAM). It has built in Wi-Fi and Bluetooth 4.2 which makes it ideal for this project. The board has a 40 pin general-purpose input/output (GPIO) header allowing for inter-connectivity between the different modules in the project. There are also 3 ports on the board, one for HDMI and the other 2 for micro-USB.
### Anavi Infrared pHAT
The Anavi Infrared pHAT allows the Raspberry Pi to utilise infrared technologies though the use of its transmitters a receiver. This board has a 40 pin GPIO header and also contains sensor modules for temperature, humidity, barometric pressure and light.
### Waveshare PN532 NFC HAT
The Waveshare PN532 is a Raspberry Pi HAT designed to allow development boards to utilise Near Field Communications (NFC) and Radio Frequency Identification (RFID) technologies. The HAT has a 40 pin GPIO header and supports various NFC and RFID cards such as MIFARE and NTAG2.
### Battery (?)
## Software Technology Stack
*Insert Software Architecture here!*
### Raspberry Pi OS

Raspberry Pi OS is the officially supported operating system for the Raspberry Pi. Installing Pi OS is extremely easy, as Raspberry Pi provide an imager to flash the operating system onto an SD card so that it can be used on the board.
The operating system comes in two different installations, those being the Desktop and Lite versions. Both versions are based on Debian, however the two images vary. The Desktop version of the operating system comes as a standard desktop operating system, with some of the main features being it’s graphical user interface (GUI), web browser, media player and even an integrated development environment (IDE).
The Lite version of the operating system is much more bare bones, coming only with a command line interface. Because of this it is faster than it’s Desktop counterpart and allows for much more customizability, however the lack of a GUI and it’s reliability on the command line means that it is less intuitive to use.
# Sequence Diagrams
# Screens
# References